## Slide 1
ELEN90096 HARDWARE ACCELERATED COMPUTING · PROJECT STATUS UPDATE
FPGA-Accelerated SRCNN on Kria KV260
Vitis HLS · AXI4-Stream DATAFLOW · AXI DMA · PYNQ
Ziye Xiong · Aero Cao
Status HLS, RTL verification and 200 MHz hardware are complete; Q24.8 and Q20.12 both pass bit-exact on the KV260 board.
✓ Software
Golden + host
✓ HLS
OC4 · 5 ns
✓ RTL
independent TB
✓ Vivado
routed 200 MHz
✓ Board
Q24.8 + Q20.12 PASS
Notes: Presenter 1 — Ziye Xiong | Suggested time: 0:45 Hi everyone. I'm Ziye Xiong. This is Aero Cao. Our project is an FPGA accelerator for SRCNN. SRCNN is a network for image super-resolution. We run it on the Kria KV260 board. Here is our status in one line. The HLS design is done. The RTL verification is done. The 200 MHz hardware is done. And both fixed-point versions now pass on the real board. The bar at the bottom shows all five stages complete. For each part, we answer four questions. What did we build? Why? What is the evidence? What is still missing?

## Slide 2: SRCNN: three fixed conv layers, 255 × 255 in and out
Input is already bicubic-upsampled; the accelerator performs inference only — the network itself cannot be changed.
Input
1 × 255 × 255
Conv1
9 × 9
1 → 64
ReLU
F1
64 × 255 × 255
Conv2
1 × 1
64 → 32
ReLU
F2
32 × 255 × 255
Conv3
5 × 5
32 → 1
no activation
Output
1 × 255 × 255
Stride = 1
all three layers
Cross-correlation
kernels are not flipped
Replicate-edge padding
spatial size preserved
Notes: Presenter 1 — Ziye Xiong | Suggested time: 0:50 The network is fixed by the course. We cannot change the algorithm. We can only change how it runs. The input has one channel. It is 255 by 255 pixels. It is already upsampled with bicubic. Conv1 has 64 filters. Each filter is 9 by 9. ReLU follows. Conv2 is a 1 by 1 convolution. It turns 64 channels into 32. ReLU follows again. Conv3 has a 5 by 5 kernel. It turns 32 channels into one image. It has no activation. All layers use stride 1. We use cross-correlation. So the kernels are not flipped. Borders use replicate-edge padding. So the output is also 255 by 255.

## Slide 3: 522 M MACs per frame — Conv1 dominates
Chart: MACs per frame (millions)
| Conv1 | Conv2 | Conv3
MACs per frame | 337.09 | 133.17 | 52.02
522,280,800
MAC per 255 × 255 frame · Conv1 = 64.54 %
Fits hardware
Regular convolutions
High input reuse
Parallel output channels
Layers can pipeline
Challenges
Large intermediate maps
Deep sums (Conv3: 800 terms)
DDR / DMA traffic
Fixed-point precision
Notes: Presenter 1 — Ziye Xiong | Suggested time: 0:55 Now let's count the work. One frame needs about 522 million MACs. MAC means multiply-accumulate. Conv1 alone needs 337 million. That is about 65 percent. So Conv1 is our first target. This workload fits hardware well. The convolutions are regular. Each input pixel is reused many times. The 64 output channels are independent. So they can run in parallel. The three layers can also form a pipeline. There are also challenges. The middle feature maps are large. Conv3 adds 800 terms for each output. So the accumulator must be wide. DDR and DMA traffic can become a bottleneck. And fixed-point precision must be proven.

## Slide 4: One streaming pass: feature maps never touch DDR
PS · DDR
PL · srcnn_axis_dataflow_top (200 MHz)
Model buffer
8,129 words · 32,516 B
Input frame
65,025 × 32-bit
Output frame
65,025 × 32-bit
load_runtime_model
Layer-local weights + bias (on-chip, loaded once per run)
MM2S
Conv1 OC4
FIFO
Conv2
FIFO
Conv3
S2MM
AXI4-Stream, 32-bit words, TLAST at frame end
AXI DMA (simple mode, 26-bit length)
Pixel-major stream
each pixel carries its channel vector between layers — no full CHW feature map
DDR holds only model, input, output
model loaded once; Conv1 + Conv2 maps (~23.81 MiB at 32-bit) never written back
Notes: Presenter 1 — Ziye Xiong | Suggested time: 1:15 This is our final architecture. The left side is the PS. Its DDR holds three buffers. One is the model. One is the input frame. One is the output frame. First, a block called load_runtime_model reads the model from DDR. The model has 8,129 words. That is 32,516 bytes. It is read once per run. Each layer then keeps its own weights on chip. Next, the image streams in through AXI DMA. It is 65,025 words of 32 bits. Conv1 has four output-channel lanes. Conv1 feeds Conv2 through a FIFO. Conv2 feeds Conv3 through another FIFO. The result streams out through DMA. The output is also 65,025 words. The key idea is the pixel-major stream. Each pixel travels with all its channel values. We never build a full feature map. So the Conv1 and Conv2 maps are never written to DDR. Together they would be about 24 MiB. DDR only holds the model, the input and the output.

## Slide 5: HLS optimisation: fix timing first, then parallelise
1
Natural loops
Functional baseline vs Golden
2
Line buffer
Rows streamed; circular banks
3
Fixed-delay line buffer
No runtime bank selector
4
Replicate-only
Compile-time padding; 5 ns restored
5
Conv1 OC2
2 output channels / pass
6
Conv1 OC4
4 output channels / pass
7
Canonical DATAFLOW
AXIS + FIFOs between layers
What drove the changes
Circular bank selector → wide muxes → timing
Fixed-delay banks: one permanent role each
Replicate-only: 5 ns HLS timing restored
Kept negative result: write-back address change, no gain
Timing repair
Parallelism
Structure
Notes: Presenter 1 — Ziye Xiong | Suggested time: 1:10 We reached this design in several steps. After each step, we checked against the Golden. Step one was natural loops. This was our functional baseline. Step two added line buffers. Our first line buffer used circular row banks. A runtime selector picked the bank. This selector made wide multiplexers. The multiplexers hurt timing. So we used fixed-delay banks. Each bank has one fixed role. The selector is gone. Then we specialised the code for replicate padding only. This happens at compile time. It brought back 5 ns HLS timing. Only then did we add parallelism. First we computed two output channels per pass. Then we computed four. Last, we built a canonical DATAFLOW structure. Streams connect the layers. One idea did not help. We changed the write-back address logic. It gave no gain. We kept it as a negative result. HANDOVER: "Timing is now under control. Aero will show what OC4 gives us, and how we got it onto the board."

## Slide 6: Conv1 OC4 cuts estimated HLS latency by 54.8%
Chart: HLS latency estimate (million cycles @ 5 ns)
| Top latency | Conv1 latency
MAC-A | 457.51 | 360.37
OC4 | 206.91 | 109.78
−54.8%
Top latency
−69.5%
Conv1 latency
Resource | MAC-A | OC4
DSP | 13 | 25
LUT | 13,982 | 15,960
All 64 kernels still computed — 4 output channels per pass (16 groups × 81 taps, II = 1).
Scope: Vitis HLS C-synthesis estimates at 5 ns — not board measurements (board timing: Slide 9).
Notes: Presenter 2 — Aero Cao | Suggested time: 0:50 Thanks, Ziye. This slide compares two designs. MAC-A is our timing-clean design without parallelism. OC4 is the parallel design. The top latency drops from 457.5 million cycles to 206.9 million. That is 54.8 percent lower. Conv1 latency is 69.5 percent lower. We still compute all 64 kernels. OC4 just computes four output channels per pass. The cost is more hardware. DSPs go from 13 to 25. LUTs go from about 14 thousand to 16 thousand. Please note one thing. These are HLS estimates. They are not board measurements.

## Slide 7: Q20.12 recovers float quality; Q24.8 does not
Chart: Reconstruction PSNR vs fractional bits (W = 32)
| 8 | 10 | 12 | 14 | 16 | 18 | 20
Set14 subset mean (fixed) | 25.706 | 29.128 | 29.157 | 29.158 | 29.159 | 29.158 | 29.158
Float reference (29.158 dB) | 29.158 | 29.158 | 29.158 | 29.158 | 29.158 | 29.158 | 29.158
Butterfly (fixed) | 25.165 | 27.475 | 27.474 | 27.477 | 27.477 | 27.477 | 27.477
Q24.8
FAILS GATE
Butterfly 27.48 → 25.16 dB
Set14 mean 29.16 → 25.71 dB
1,205 / 5,184 non-zero Conv1 weights → 0
Q20.12
SELECTED
Max PSNR Δ vs float: 0.004187 dB
Min fixed-vs-float PSNR: 60.621 dB
Lowest tested precision passing gate
Q24.8 is arithmetically correct but too coarse. Raw words and bitstreams of the two profiles are not interchangeable. Data: Butterfly + 13 supplied Set14 images.
Notes: Presenter 2 — Aero Cao | Suggested time: 1:05 Next is precision. Our first format was Q24.8. Its arithmetic is correct. But its quality is too low with the official weights. Butterfly drops from 27.48 dB to 25.16 dB. The Set14 mean drops from 29.16 dB to 25.71 dB. Why? Q24.8 has only 8 fractional bits. So 1,205 of 5,184 non-zero Conv1 weights become zero. So we tested more fractional bits offline. The chart shows the result. At 12 fractional bits, we get Q20.12. The largest PSNR difference from float is 0.004 dB. The lowest fixed-versus-float PSNR is 60.6 dB. Q20.12 is the lowest precision we tested that passes our criteria. The two formats use different raw words and bitstreams. So we never mix them.

## Slide 8: Verified at every level, up to the board
✓ Golden / independent oracle
✓ Host C simulation
✓ HLS synthesis (5 ns)
✓ Independent RTL testbench
✓ Vivado routed implementation
✓ KV260 board run
Vitis automatic co-simulation
1 × 1 and 5 × 7 PASS · 13 × 17: auto harness stalled → not passed
Independent SystemVerilog AXI testbench
13 × 17 dynamic and fixed modes: PASS
Q20.12: 2 full 255 × 255 frames, no DUT reset, changed input + model
130,050 / 130,050 outputs bit-exact
Corrupted Golden is rejected by the scoreboard
Open: root cause of the auto-harness stall — the RTL is covered by our testbench and by the board run.
Notes: Presenter 2 — Aero Cao | Suggested time: 1:05 How do we know the hardware is correct? We check it level by level. The base is an independent Golden. Then come host C simulation and HLS synthesis. The RTL level needs care. Vitis automatic co-simulation passed 1 by 1 and 5 by 7. But on 13 by 17, its harness stalled. So that run did not pass. So we wrote our own SystemVerilog testbench. It tests the generated RTL directly. For Q20.12, it runs two full frames without a reset. All 130,050 outputs match bit for bit. A wrong Golden is rejected. So the check really works. The top level is now green too. Both formats passed on the real KV260. I will show that next. The co-sim stall's root cause is still open. But the RTL is checked by our testbench and by the board.

## Slide 9: Both V3 overlays pass bit-exact on the KV260
V3 routed (5.000 ns) | Q24.8 | Q20.12
Setup WNS | +0.105 ns | +0.109 ns
LUT | 16,087 | 16,328
FF | 17,377 | 18,020
BRAM tiles | 97 | 97.5
DSP | 86 | 86
V2 → V3 fix auxiliary reset was tied low and held AXI in reset; V3 ties it high.
KV260 BOARD RUN · EACH FORMAT
14 / 14
frames PASS
0.750 s
median per frame
Every frame: 65,025 / 65,025 output words match the fixed-point Golden
Warm-up
10 repeats
New input + model
Restored
Overlay reload
Median: Q24.8 0.7498 s · Q20.12 0.7499 s · P95 ≈ 0.750 s
Scope: host-observed transfer start → done, including model load and DMA — not kernel-only, and not a CPU speedup. Bit-exact means equal to the fixed-point Golden, not zero error versus float.
Notes: Presenter 2 — Aero Cao | Suggested time: 1:05 This is the board result. We built final V3 overlays for both formats. Both close timing at 5 nanoseconds, or 200 megahertz. The slack is 0.105 and 0.109 nanoseconds. Resources are almost the same. Our first board build, V2, did not work. We found the cause. An auxiliary reset input was tied low. This held the AXI fabric in reset. V3 ties it high. Then both formats worked. Each format ran 14 frames. That includes a warm-up and 10 repeats. It includes a new input and model, a restore, and an overlay reload. All 65,025 words in every frame match the fixed-point Golden. The median time is about 0.750 seconds per frame. This includes model loading and DMA. It is not kernel-only time. Bit-exact here means equal to the fixed-point Golden. It does not mean zero error versus float.

## Slide 10: Board gate passed — next: fair CPU comparison
COMPLETED
✓ Golden and host verification
✓ Line-buffered OC4 accelerator
✓ AXI-Stream / DATAFLOW datapath
✓ Q20.12 precision profile
✓ Full-frame independent RTL validation
✓ 200 MHz routed V3 implementation
✓ KV260: Q24.8 + Q20.12 PASS (14 frames each)
✓ Repeats, new model, overlay reload
REMAINING — TOWARD THE FINAL REPORT
1
Fair CPU baseline, same measurement boundary
2
Performance breakdown of the 0.750 s
3
Board validation on more images
4
Final report
Takeaway Both formats take the same board time; Q20.12 stays far closer to float quality. No CPU speedup is claimed until the fair baseline is measured.
Questions?
Notes: Presenter 2 — Aero Cao | Suggested time: 0:50 So where are we now? The left side is done. It goes from the Golden all the way to the board. Both Q24.8 and Q20.12 pass on the KV260. Four tasks remain. First, a fair CPU baseline with the same measurement boundary. Only then can we claim a speedup. Second, a performance breakdown of the 0.750 seconds. Third, board checks on more images. Fourth, the final report. Both formats take the same board time. But Q20.12 is much closer to float quality. Thank you. We are happy to take questions.